## Slide 1: Lecture 18: Introduction to MRI Principle
Dr. Guohua Cao （曹国华） caogh@shanghaitech.edu.cn
School of Biomedical Engineering
ShanghaiTech University
4/9/2023

## Slide 2: Nuclear magnetic resonance exploits a property of the nucleus called spin.
Spin is related to the angular momentum of the nucleus and each subatomic particle.
Spin is a quantum mechanical property, which means it has discrete quantized states.
Nuclear Spin, I, is the total angular momentum of the nucleus.
The Nuclear Spin ranges from 0 to 7 in half integers.
The total number of different spin states is 2I+1

## Slide 3: A nucleus has spin if it has either an odd number of protons or neutrons.
http://www.bruker-nmr.de/guide/eNMR/chem/NMRnuclei.html
Notes: Nuclear (like 4He, 12C, and 32S) with even numbers of both protons and neutrons have I = 0 and possess no net angular momentum

## Slide 4: An example from the eNMR Periodic Table showing the isotopes of Hydrogen.
Notes: Angular momentum changes in whole units.

## Slide 5: total magnetic spin in a voxel
w/o external magnetic field
w. external magnetic field, B0
null net magnetization
Some of the spins align with the field (parallel) and some align against the field (anti-parallel).

## Slide 6: Precession：进动
陀螺仪的进动
Precession of Gyroscope
Spin Precession
wobble (or precess) about the axis

## Slide 7: Precession Frequency i.e. Larmor Frequency
Magnetic moments precess in a magnetic field.
Larmor frequency: frequency of precession and resonance, usually in the radiofrequency (RF) range
ω0 = γ B0

## Slide 8
Magnetic Resonance Imaging (MRI) measures the precession of spins in a magnetic field to produce “images” that yield structural, physiological, and/or chemical information.
Perfusion
Diffusion
Spectroscopy
Structural
Structural –HE3
Flow
Functional
Notes: Questions that will be answered through out this course?
What is a “spin”?
Why did you use the word “spin” instead of “proton” or “water”?

## Slide 9: Why are the spins not EXACTLY aligned with the magnetic field?
http://www.chem.umn.edu/groups/harned/classes/8361/lectures/NMR.pdf
Notes: Quantum Mechanis:
http://www.quantumdiaries.org/2011/09/17/angular-momentum-in-quantum-mechanics/

## Slide 10: Heisenberg Uncertainty Principle states that if we know one component of the angular momentum exactly then we know nothing about the other two components.
This subtle but very important point is often not explained. The magnetic moment of a spin is drawn as a cone or at at an angle to the magnetic field.
For more information see http://www.quantumdiaries.org/2011/09/17/angular-momentum-in-quantum-mechanics/
http://www.chem.umn.edu/groups/harned/classes/8361/lectures/NMR.pdf
Notes: http://www.quantumdiaries.org/2011/09/17/angular-momentum-in-quantum-mechanics/

## Slide 11: We can decompose the net magnetic moment into its three components: Mx, My, and Mz
The magnetic vector of spinning protons can be broken down into two orthogonal components: a longitudinal or Z component, and a transverse component, lying on the XY plane.
Precession corresponds to rotation of the transverse component about the longitudinal axis.

## Slide 12: Net magnetization in Z axis and XY plane
Spins do not rotate in phase, thus null transverse macroscopic magnetization.
More spins aligned with the field than spins aligned against the field

## Slide 13: There is no Net Magnetic Moment along the X and Y direction because “classically” the individual magnetic moments have random orientations.

## Slide 14: A Net Magnetic Moment along the Z direction is created by the external magnetic field according to the Boltzmann Distribution.
Magnetic moments align relative to a magnetic field in discrete number of energy states.

## Slide 15: Boltzmann Distribution
parallel - low energy state
B0
anti-parallel - high energy state
Nup / Ndown = Proportion of parallel / antiparallel spins
γ = Gyromagnetic ratio
h = Planck's constant / 2π
k = Boltzmann's constants
T = Temperature (in Kelvins)
B = Intensity of static magnetic field (Teslas)

## Slide 16: Nuclear Magnetic Resonance (NMR)
Resonance is exchange of energy between two systems at a specific frequency.
Magnetic resonance corresponds to the energetic interaction between spins and electromagnetic radiofrequency (RF).
Only protons that spin with the same frequency as the electromagnetic RF pulse will respond to that RF pulse.
Excitation: There is a modification of spin equilibrium and absorption of electromagnetic energy by atomic nuclei, which is called excitation.
Relaxation: When the system returns from this state of imbalance to equilibrium (relaxation), there is an emission of electromagnetic energy.

## Slide 17: Excitation
During excitation, longitudinal magnetization decreases and a transverse magnetization appears (except for a 180° flip angle).
  Longitudinal magnetization is due to a difference in the number of spins in parallel and anti-parallel state. Transverse magnetization is due to spins getting into phase coherence.
The flip angle depends on the strength and duration of the electromagnetic RF pulse.

## Slide 18: 90°flip angle
Notes: There is no longitudinal magnetization (equal proportion of parallel and anti-parallel spins)
A transverse magnetization exists (all spins are in phase: complete phase coherence)

## Slide 19: Relaxation
Return to equilibrium of net magnetization is called Relaxation. During relaxation, electromagnetic energy is retransmitted: this RF emission is called the NMR signal.
Relaxation combines 2 different mechanisms:
  Longitudinal relaxation corresponds to longitudinal magnetization recovery
  Transverse relaxation corresponds to transverse magnetization decay
Notes: Return to equilibrium of net magnetization is called Relaxation. During relaxation, electromagnetic energy is retransmitted: this RF emission is called the NMR signal. Relaxation combines 2 different mechanisms:
Longitudinal relaxation corresponds to longitudinal magnetization recovery
Transverse relaxation corresponds to transverse magnetization decay

## Slide 20: T1 Relaxation (Longitudinal relaxation)
After time T1, longitudinal magnetization has returned to 63 % of its final value.
Notes: Longitudinal relaxation is due to energy exchange between the spins and surrounding lattice (spin-lattice relaxation), re-establishing thermal equilibrium. As spins go from a high energy state back to a low energy state, RF energy is released back into the surrounding lattice.
The recovery of longitudinal magnetization follows an exponential curve. The recovery rate is characterized by the tissue-specific time constant T1. After time T1, longitudinal magnetization has returned to 63 % of its final value. With a 1.5 T field strength, T1 values are about 200 to 3000 ms. T1 values are longer at higher field strengths.

## Slide 21: T1 Relaxation
T1
T1 Relaxation exchanges energy with the environment

## Slide 22: T2 Relaxation (Transverse relaxation)
After time T2, transverse magnetization has lost 63 % of its original value.
Notes: Transverse relaxation results from spins getting out of phase.
As spins move together, their magnetic fields interact (spin-spin interaction), slightly modifying their precession rate. These interactions are temporary and random.
Thus, spin-spin relaxation causes a cumulative loss in phase resulting in transverse magnetization decay. Transverse magnetization decay is described by an exponential curve, characterized by the time constant T2. After time T2, transverse magnetization has lost 63 % of its original value.

## Slide 23: T2 Relaxation decays exponential and determines how long one is able to detect the spins in the transverse plane.
T2 Relaxation spins exchanges energy with each other. (Loss of coherence)
T2

## Slide 24: Excitation & Relaxation Combined
Notes: MRI signal is generated during the relaxation.

## Slide 25: Excited spins want to return to thermal equilibrium – aligned along the main magnetic field.
T1 relaxation describes how fast the spins align with the magnetic field.
T2 relaxation describes how fast spins lose spin coherence.

## Slide 26: T2 Relaxation is a fundamental property of the material.
Random fluctuations in local magnetic field seen by the nucleus result in a random change to the precession frequency of the spins

## Slide 27: T2* Relaxation
Is not an intrinsic property of the tissue/substance but is relaxation due to the inhomogeneity of the magnetic field
  Homogeneity is the uniformity of the magnetic field over a given volume (sphere)
  Measured in parts per million (ppm)
  Typical magnet ±2.5 ppm over 40 cm
  Temporal and temperature stability
Notes: http://eu.amershamhealth.com/medcyclopaedia/Volume%20I/PARTS%20PER%20MILLION%20%20PPM%20.asp
Parts per million (PPM),
term used in MR imaging to define the quality of the magnetic field homogeneity or the chemical shift of a substance investigated. A field inhomogeneity of 10 ppm in a field of 1.5 Tesla thus means maximum field strength variations of 1.5 10 5 Tesla or 0.15 gauss. Since magnetic field and resonant frequency are proportional (Larmor equation), an inhomogeneity of 1 ppm also translates into Larmor frequency variation of 63.9 Hz at 63.9 MHz.

## Slide 28: Relationship between T2 and T2*
T2’ is the relaxation constant due to magnetic field inhomogeneity alone
T2 Relaxation
T2* Relaxation

## Slide 29: Image contrast in MRI can be achieved by acquiring data with different MRI pulse sequences, which act as filters, and counting spins (longitudinal or transverse direction) at each and every voxel.
MRI pulse sequence
Input
Filter
Output
Spin
Image
MRI Pulse
Sequence

## Slide 30: The MRI pulse sequence acts as a filter that selects the information that we are interested in measuring.
Tissue
Properties
Proton
Density
T2
Weighted
T1
Weighted
Pulse Sequence

## Slide 31
All imaging devices have three things in common
  An energy source
  An object which alters the energy source
  A detector which measures the altered energy source intensity and position.

## Slide 32: X-Ray scanners count the number of X-rays that pass through an object.
Object
X-Ray Source
X-Ray Detector
100
100
100
10
Notes: 1) http://science.howstuffworks.com/x-ray1.htm

## Slide 33: MRI counts the number of energized spins at a particular location.
MRI energy source is radio frequency (RF) waves
In a magnetic field, protons in the object that have spin absorb the energy from the radio waves
We detect the spins as they release the energy they just absorbed and return to thermal equilibrium.
The position of the spins in the object is determined by from it’s precession frequency.
RF Source
Object
Object
RF Detector
Notes: Tuning Fork Analogy

## Slide 34: http://www.imaios.com/en/e-Courses/e-MRI