## Slide 1: Lecture 2: Foundation of Biomedical Imaging
2/27/2024
Dr. Guohua Cao （曹国华） caogh@shanghaitech.edu.cn
School of Biomedical Engineering
ShanghaiTech University

## Slide 2: Lecture 2: Foundation of Biomedical Imaging
Common concepts in biomedical imaging
  United view of imaging technologies
  Current clinical practice of medical imaging
  Image Storage: PACS & DICOM
Introduction to ImageJ
  An image is a matrix!
  Histogram
  Image Display: Display Monitor, Window/Level
  Image normalization
Terminologies in 2D & 3D imaging
  Axial, Coronal, Sagital
  MPR, Curved MPR, Volume Rendering, MinIP/AIP/MIP

## Slide 3: Medical Imaging Modalities
List of major medical imaging modalities:
  X-rays
  CT (Computed Tomography)
  MRI (Magnetic Resonance Imaging)
  US (Ultrasound)
  PET (Positron Emission Tomography)
  SPECT (Single-Photon Emission Computed Tomography)
Multi-Modalities:
  PET/CT
  SPECT/CT
  PET/MRI
  …
Notes: 2D vs 3D

## Slide 4: Unified view of imaging technologies

## Slide 5
X-ray
SPECT
Ultrasound
CT
MRI
PET
医学影像设备
~
温度计

## Slide 6: In dream - a Push-button Solution!
Acquisition
Reconstruction & Processing
Interpretation

## Slide 7: In reality, not there yet, but pretty cool.
Picture archiving and communication system (PACS)

## Slide 8: Image Storage: PACS & DICOM
A picture archiving and communication system (PACS) is a medical imaging technology which provides economical storage and convenient access to images from multiple modalities. Electronic images and reports are transmitted digitally via PACS; this eliminates the need to manually file, retrieve, or transport film jackets, the folders used to store and protect X-ray film. The universal format for PACS image storage and transfer is DICOM (Digital Imaging and Communications in Medicine).
DICOM is the standard for the communication and management of medical imaging information and related data. Also known as NEMA standard PS3, and as ISO standard 12052:2017 "Health informatics – Digital imaging and communication in medicine (DICOM) including workflow and data management“. DICOM standard is held by The National Electrical Manufacturers Association (NEMA) in the U.S.

## Slide 9: Lecture 2: Foundation of Biomedical Imaging
Common concepts in biomedical imaging
  United view of imaging technologies
  Current clinical practice of medical imaging
  Image Storage: PACS & DICOM
Introduction to ImageJ
  An image is a matrix!
  Histogram
  Image Display: Display Monitor, Window/Level
  Image normalization
Terminologies in 2D & 3D imaging
  Axial, Coronal, Sagital
  MPR, Curved MPR, Volume Rendering, MinIP/AIP/MIP

## Slide 10: ImageJ
http://imagej.nih.gov/ij/
Useful for import/export, display, edit, and simple math including histogram & line intensity profile.
Excise yourself: Get your hands-on ImageJ.

## Slide 11: An image is a matrix!

## Slide 12: Histogram

## Slide 13: Line Intensity Profile

## Slide 14: Important Metric of Display Monitor
Resolution
  Pixel size/pitch, Retina display
  Display size, 2k, 4k, 8k
Grey-scale/Color-scale range
  Bit depth, 8-bit, 12-bit, 16-bit
  Gamma curve
Luminance/brightness
  Luminance is defined as the ‘absolute quantity of radiation emitted from a given source of visible electromagnetic radiation.
  Medical displays provide much higher luminance than consumer displays.
Contrast Ratio
  Defined as the ratio of the white luminance to black luminance.
Viewing angle, Refresh rate, Response time, uniformity/bad pixels.
Notes: https://www.ncbi.nlm.nih.gov/pmc/articles/PMC2765178/

## Slide 15: Display Monitor Color Scale
grayscale
color scale
Display Monitor
Monitors are typically RGB-colored devices, with separate red, green, and blue dots. Each dot can be set to 256 different brightness levels (8 bits), so 24 bits define a color (16 million possible RGB colors).
To get grayscale, you set all three colors to the same value, so there are only 256 possible shades of gray.
Notes: Monitor color depth, ADC bit depth

## Slide 16: Why 256?
Human eyes normally can only perceive up to 256 shades of grey (i.e. human limit).
  Professional diagnostic monitor can have >256 (8 bits) grey scales.
Medical images are inherently grey-scale images, but pseudo colors can be used to render “realistic” images.
Notes: Pseudo colors = 伪彩色

## Slide 17: Gamma Curve of Display Devices
Gamma curve – the mapping of the image/pixel intensity to the brightness of the display device.
Vin
Vout

## Slide 18: Image Display Window & Level
The range pixel values in medical images can be >> 256.
To display a medical image,
Range of the pixel numbers = Window Width (WW)
Center of the range =
Window Level (WL)
x
x is displayed as
white, if x > WL + (WW ÷ 2).
blacks if x < WL - (WW ÷ 2).
shades of grey
That is, normalized to [0, 255].
the upper grey level (x) is calculated via WL + (WW ÷ 2).
the lower grey level (y) is calculated via WL - (WW ÷ 2).
Change WW and WL will change image contrast and brightness, respectively.
  WW controls contrast; Larger WW leads to smaller contrast.
  WL controls brightness.

## Slide 19: Window/Level Example
L - display window level
W - display window width
Imax - maximum intensity scale of the display device (for an 8-bit display device, Imax = 255).
Mapping function:

## Slide 20: Image Normalization
Given an image f(x), where the range of pixel values is.
To normalize the image, f(x), into another range of pixel values as ,

## Slide 21: Lecture 2: Foundation of Biomedical Imaging
Common concepts in biomedical imaging
  United view of imaging technologies
  Current clinical practice of medical imaging
  Image Storage: PACS & DICOM
Introduction to ImageJ
  An image is a matrix!
  Histogram
  Image Display: Display Monitor, Window/Level
  Image normalization
Terminologies in 2D & 3D imaging
  Axial, Coronal, Sagital
  MPR, Curved MPR, Volume Rendering, MinIP/AIP/MIP

## Slide 22: Imaging in 2D & 3D
2D Projection
3D Tomography
Many slices make up a volume in 3D tomographic imaging.

## Slide 23: Displaying 2D & 3D images
X-ray (2D)
Sagittal Slice (3D)
Axial Slice (3D)
Coronal Slice (3D)

## Slide 24: MPR (Multiplanar Reformation) & Volume Rendering
Reading Assignment: “Introduction to the Language of 3D Imaging with MDCT” by Dalrymple et al.
Curved Planar Reformation
right coronary artery
Minimum/Average/Maximum Intensity Projection