## Slide 1
Single Photon Imaging
Siyuan Shen

## Slide 2: What CVers are used to
Camera
Notes: What are they used for

## Slide 3: What CVers are used to
ToF camera
1）160 frames per second
2）centimeters – meters
3）X00 dollars
High-speed camera
1）X000 frames per second
2）X0000 dollars
Notes: What are they used for

## Slide 4: Where all things get started
[1] Velten, Andreas, et al. "Femto-photography: capturing and visualizing the propagation of light." ACM Transactions on Graphics (ToG) 32.4 (2013): 1-8.
Notes: 量子力学与相对论

## Slide 5: Streak camera
Notes: 光电条纹相机的工作原理是将光照到光电阴极上，当光电阴极被光子击中时通过光电效应产生电子。电子在阴极射线管中被加速，并通过由一对板产生的电场，使电子向侧面偏转。通过调节两块板之间的电动势，电场被迅速改变，使电子产生时间变化的偏转，使电子在管子末端的荧光屏上扫过。
在条纹传感器中，一个光电阴极将从扫描线的每个空间位置进入的光子转换为电子。条纹传感器根据这些电子到达的时间，将其偏转到传感器T维的不同位置，从而生成X-T图像。抵达的时间，将这些电子反射到传感器T维度上的不同位置（见图2（b）和2（c））。这是通过快速改变电极之间的扫描电压来实现的。改变传感器中电极之间的扫描电压。对于每个水平扫描线，相机记录了一个由脉冲照射的场景，并对4:5 × 108个脉冲散射的光进行了平均。脉冲（见图2（d）和2（e））。

## Slide 6: Streak camera
Time resolution: ps
Space resolution: 0.5mm
3) 1.5 trillion frames per second
4) expensive: x00000 dollar
Notes: 光电条纹相机的工作原理是将光照到光电阴极上，当光电阴极被光子击中时通过光电效应产生电子。电子在阴极射线管中被加速，并通过由一对板产生的电场，使电子向侧面偏转。通过调节两块板之间的电动势，电场被迅速改变，使电子产生时间变化的偏转，使电子在管子末端的荧光屏上扫过。
在条纹传感器中，一个光电阴极将从扫描线的每个空间位置进入的光子转换为电子。条纹传感器根据这些电子到达的时间，将其偏转到传感器T维的不同位置，从而生成X-T图像。抵达的时间，将这些电子反射到传感器T维度上的不同位置（见图2（b）和2（c））。这是通过快速改变电极之间的扫描电压来实现的。改变传感器中电极之间的扫描电压。对于每个水平扫描线，相机记录了一个由脉冲照射的场景，并对4:5 × 108个脉冲散射的光进行了平均。脉冲（见图2（d）和2（e））。

## Slide 7: Femto-photography
Challenges:
Low signal-to-noise (SNR) ratio.
Direct measurements of events appear warped in space-time.
Notes: 首先，对于一个未放大的激光脉冲，单次曝光时间小于2ps将无法收集足够的光。的时间将无法收集到足够的光，因此信噪比 将是不可行的低。举例来说，对于一个由100W灯泡照明的桌面场景 为例，对于一个由100W灯泡照亮的桌面场景，在2ps的开放时间内，平均只有约1个光子到达传感器。在2ps的开放快门期间到达传感器。

## Slide 8: Femto-photography System

## Slide 9: Femto-photography System

## Slide 10: What can we see

## Slide 11: What can we see

## Slide 12: What’s abnormal

## Slide 13: What’s abnormal

## Slide 14: Time Unwarping

## Slide 15: Time-Unwarped Image

## Slide 16: More results

## Slide 17: Streak camera
1) Time resolution: femtoseconds
2) 1.5 trillion frames per second
3) expensive: x00000 dollar
Notes: 光子马赫锥”和神经元激发（neurons fire
2011年12月，麻省理工学院的一个团队发布了结合使用条纹相机和重复激光脉冲的图像，模拟出每秒一万亿帧的电影。[6] 2020年，加州理工学院的一个团队超越了这个数字，实现了每秒70万亿帧的帧率。）

## Slide 18: Here comes NLOS
Notes: 量子力学与相对论

## Slide 19: The first NLOS
[2] Velten, Andreas, et al. "Recovering three-dimensional shape around a corner using ultrafast time-of-flight imaging." Nature communications 3.1 (2012): 1-8.
d
Notes: 量子力学与相对论

## Slide 20: Why NLOS difficult
measurements
Transport matrix
Unknown volume
Problem: extremely large
1) for n=100, has 1 trillion elements
2) for n=1000, sparse A needs petabytes of memory

## Slide 21: FBP for NLOS
Notes: 量子力学与相对论

## Slide 22: FBP for NLOS
Notes: 量子力学与相对论

## Slide 23: FBP for NLOS
Process:
Set bounding box
FBP
Re-set bounding box and repeat
Using Laplace kernel
Notes: 量子力学与相对论

## Slide 24: FBP for NLOS
Notes: 量子力学与相对论

## Slide 25: The first con-focal NLOS
Contribution:
1) Confocal NLOS
2) Light Cone Transform
Assumption:
1) Isotropic scattering (only diffuse or retroreflective objects)
[3] O’Toole, Matthew, David B. Lindell, and Gordon Wetzstein. "Confocal non-line-of-sight imaging based on the light-cone transform." Nature 555.7696 (2018): 338-341.
Notes: 这篇文章的重点主要有两点。一点是LCT第一次正式提出了confocal的NLOS这一setting。
还有就是light cone transform 这一核心方法。这一方法能够为解决NLOS的这一inverse problem提供一种效果较好且速度较快且memory efficienct的方法。

## Slide 26: Here comes NLOS
Notes: 量子力学与相对论

## Slide 27: Single-photon avalanche diode
Notes: SPAD是PN结工作在Geiger模式下，这种模式下p-n结反向偏置电压在击穿电压(Break Down)之上。当一个光子被半导体的耗尽区吸收时，它会产生一个电子-空穴对，这个电子-空穴对在电场的作用下分裂和加速。如果电子或空穴的能量足够高，撞击电离就会产生更多的电子-空穴对，引发自我维持的雪崩。当电场强度高于材料的临界场时，载流子的撞击电离就会发生这种雪崩现象。在硅中，临界场Ecr≈3×105v /cm。通常一旦雪崩开始一股毫安级的大电流就会流经设备，直到它被摧毁。如下图,因此一般会使用电阻Rq与SPAD串联防止烧毁的情况.这种电阻通常是千欧姆的量级.并行当V-A的阳极电压向过量偏置电压V-EB增加时，它通过将电流降低到小于100 μA 的方式来抑制(quenching )雪崩。抑制(quenching )完成后，开始充电过程，使像素回到空闲模式,进入下一个周期。

## Slide 28: Single-photon avalanche diode
Time resolution: 16ps
Advantage: cheaper
Problem: noise
Notes: SPAD是PN结工作在Geiger模式下，这种模式下p-n结反向偏置电压在击穿电压(Break Down)之上。当一个光子被半导体的耗尽区吸收时，它会产生一个电子-空穴对，这个电子-空穴对在电场的作用下分裂和加速。如果电子或空穴的能量足够高，撞击电离就会产生更多的电子-空穴对，引发自我维持的雪崩。当电场强度高于材料的临界场时，载流子的撞击电离就会发生这种雪崩现象。在硅中，临界场Ecr≈3×105v /cm。通常一旦雪崩开始一股毫安级的大电流就会流经设备，直到它被摧毁。如下图,因此一般会使用电阻Rq与SPAD串联防止烧毁的情况.这种电阻通常是千欧姆的量级.并行当V-A的阳极电压向过量偏置电压V-EB增加时，它通过将电流降低到小于100 μA 的方式来抑制(quenching )雪崩。抑制(quenching )完成后，开始充电过程，使像素回到空闲模式,进入下一个周期。

## Slide 29: Confocal NLOS
Non confocal

## Slide 30: Confocal NLOS
Non confocal
Confocal

## Slide 31: Light Cone Transform

## Slide 32: Light Cone Transform
Let use
Discretize:
We can get:

## Slide 33: Why con-focal
: signal/image with noise
: kernel
: noise
: signal/image with noise
Simplified NLOS:
Wiener Filter:

## Slide 34: Light Cone Transform

## Slide 35: Light Cone Transform

## Slide 36: Light Cone Transform

## Slide 37: Light Cone Transform

## Slide 38: Result

## Slide 39: Result

## Slide 40: Result

## Slide 41: D-LCT
[4] Young, Sean I., et al. "Non-line-of-sight surface reconstruction using the directional light-cone transform." Proceedings of the IEEE/CVF Conference on Computer Vision and Pattern Recognition. 2020.
Notes: 2020 CVPR

## Slide 42: D-LCT
1) More accurate forward model with Lambert cosine law
2) Enables recovery of surface normals
Notes: 2020 CVPR

## Slide 43: Result
Notes: 2020 CVPR

## Slide 44: Result
Notes: 2020 CVPR

## Slide 45: Result
Notes: 2020 CVPR

## Slide 46: F-K
[6] Lindell, David B., Gordon Wetzstein, and Matthew O'Toole. "Wave-based non-line-of-sight imaging using fast fk migration." ACM Transactions on Graphics (ToG) 38.4 (2019): 1-13.
Notes: 2020 CVPR

## Slide 47: F-K
Notes: 2020 CVPR

## Slide 48: F-K
Notes: 2020 CVPR

## Slide 49: F-K
Algorithm:
Fast and memory efficient
Robust to specular and other complex reflectance properties
System:
Pulse Width: 30.6ps(200ps) -> 35ps(70ps)
Power: 0.11mW -> 1W (500mW)
System-wall distance: 2m -> about 4m
Object size: 0.76m * 0.51m -> about 1m * 1m
Notes: 2020 CVPR

## Slide 50: specular
Notes: 2020 CVPR

## Slide 51: specular
Notes: 2020 CVPR

## Slide 52: Result
Notes: 2020 CVPR

## Slide 53: Phasor field
[7] Liu, Xiaochun, et al. "Non-line-of-sight imaging using phasor-field virtual wave optics." Nature 572.7771 (2019): 620-623.
Notes: 2020 CVPR

## Slide 54: Phasor field
Notes: 2020 CVPR

## Slide 55: Phasor field
System:
Pulse Width: 35ps(70ps) -> 35ps(65ps)
Time bin: 16ps -> 4ps
Non-confocal
Notes: 2020 CVPR

## Slide 56: Phasor field
Notes: 2020 CVPR

## Slide 57: Fermat
[5] Xin, Shumian, et al. "A theory of Fermat paths for non-line-of-sight shape reconstruction." Proceedings of the IEEE/CVF Conference on Computer Vision and Pattern Recognition. 2019.
Notes: 2020 CVPR

## Slide 58: Space carving
[8] Kutulakos, Kiriakos N., and Steven M. Seitz. "A theory of shape by space carving." International journal of computer vision 38.3 (2000): 199-218.
Notes: 2020 CVPR

## Slide 59: Space carving in NLOS
Notes: 2020 CVPR

## Slide 60: Fermat path in NLOS
Notes: 2020 CVPR

## Slide 61: Fermat path in NLOS
Notes: 2020 CVPR

## Slide 62: Fermat path in NLOS
Notes: 2020 CVPR

## Slide 63: Neural reconstruction
[7] Grau Chopite, Javier, et al. "Deep non-line-of-sight reconstruction." Proceedings of the IEEE/CVF Conference on Computer Vision and Pattern Recognition. 2020.
Notes: 2020 CVPR

## Slide 64: Neural reconstruction
Notes: 2020 CVPR

## Slide 65: Neural reconstruction
Notes: 2020 CVPR

## Slide 66: Neural reconstruction
Problem:
Heavy memory cost
Inflexibility
Notes: Confocal nonconfoacl

## Slide 67: Neural reconstruction
Here comes NeRF
Notes: 2020 CVPR

## Slide 68: NeTF
[8] Shen, Siyuan, et al. "Non-line-of-sight imaging via neural transient fields." IEEE Transactions on Pattern Analysis and Machine Intelligence 43.7 (2021): 2257-2268.
Notes: 2020 CVPR

## Slide 69
Problem Definition
Phasor Field
F-K Migration
DLCT
DLCT [Young 20]
Phasor Field [Liu 19]
F-K [Lindell 19]
Limitations:
Fixed reconstruction resolution
Assumptions on material
Notes: There are some limitations in current methods. First the resolution of the reconstruction scenes is fixed. Most methods divide the entire space into fixed voxels based on the resolution of the input data. Some methods also limit the material of the reconstructed objects. In order to overcome these limitations, we present a novel volumetric NLOS imaging framework.

## Slide 70
MLP
Color
Density
sampling
volume rendering
Spatial location in cartesian coordinate
From NeRF to NeTF: NLOS Imaging
sampling
Scanning point location
Spatial location
density
albedo
Transients
Residual
Predicted transients
Transient rendering
Notes: Now, Let’s move on to see how we establish our neural transient fields.
First, Instead of on a line, we sample on a spherical wavefront. Then We parameterize every point under spherical coordinates. It facilitates sampling and derivation of volume rendering. However, recall that NLOS system needs to scan different spots on the relay wall, it will lead to inconsistence of spherical coordinates for the same location in the space. It will also cast challenges in network training and inference. So, We need to first transform them to their corresponding Cartesian coordinates. A multilayer perceptron takes them as input and outputs density and view dependent albedo inferences. We want to mention that the view dependent albedo enables the framework to reconstruct different materials. We then propose our transient rendering technique to predict the transient and use the difference between the predicted and real transient to optimize the multilayer perceptron.

## Slide 71
MLP
Problem Formulation under NeTF
Transient rendering
Number of particles
reflectivity of particles
Predicted
transients
Notes: Now let's take a closer look at our transient rendering technique. Our rendering model considers the density as the number of Elementary particles in space and albedo as the reflectivity of them in a certain direction.

## Slide 72
density
Propagation in Space
albedo
Reflectance:
Propagation:
Notes: In this way, The energy change of the wavefront with its propagation in space comes from the absorption and reflectance by particles.

## Slide 73
Transient Rendering Forward Model
hemisphere
Notes: So the transient at each moment is the integral of the contributions of all particles on the hemisphere corresponding to the detection point. By solving the first order differential equation, we can derive the complete transient rendering model. However, the computational cost of such a formula is very large.

## Slide 74
Simplify the Forward Model
attenuation coefficient
Notes: It mainly comes from the Attenuation coefficient. So, if we assume that the NLOS scene is all opaque and does not exhibit self-occlusions, we remove the attenuation item to simplify the fromulation, . In our experiment, we found that this formula is sufficient to get a good reconstruction result for most NLOS scenes.

## Slide 75
Integral Calculation
Uniformly sampled
Notes: Here we show how to numerically compute the continuous integral with uniformly sampled $\theta,\phi$.

## Slide 76
MLP
From NeRF to NeTF: NLOS Imaging
sampling
density
albedo
Transients
Residual
Predicted transients
Transient rendering

## Slide 77
MLP
Training and Optimization
Residual
Predicted transients
Transients
Notes: Now let’s see how we optimize our neural transient field.

## Slide 78
Training and Optimization
measurement from data
predicted measurement
Photon
count
t
Photon
count
t
Two-stage training
Hierarchical sampling
Notes: We use the L2 norm between the captured and predicted measurement as loss function. In every training batch, we use a 1D histogram from the whole 3D data. However, different from Nerf, In NLOS, SPAD only captures a sparse set of spots on the wall. So we proposed two training strategies in order to improve results. First, lets see how we deal with the training bias with two stage training.

## Slide 79
Imbalanced visibility
Two–stage Training
Loss distribution
Notes: We use a bunny for an example. Because of self-occlusion, bunny's right ear can only be observed by scanning points in the upper left corner of the wall. This means that the points on the wall are not uniform for the observation of the scene.
We show the loss distribution of the scanning points after we equally train the data. We can see the loss in the upper left corner is obviously larger than other spots. So The histogram with higher loss should be more fully trained in the following training.

## Slide 80
Two–stage Training
Loss distribution
Resample
First stage
Second stage
More balanced distribution
MCMC
Notes: Therefore, we propose that after a uniform training in the first stage, we resample the data according to the loss distribution with Monte Carlo Markov Chain. And Then we use the resampled data for the second stage training. The more balanced loss distribution will speed up network convergence and improve the result.

## Slide 81
Training and Optimization
measurement from data
predicted measurement
Photon
count
t
Photon
count
t
Two-stage training
Hierarchical sampling
Notes: now, let’s look at hierarchical sampling.

## Slide 82
Coarse uniform sampling
Hierarchical Sampling
Notes: Recall that we uniformly sample the hemisphere at each moment to calculate transient. This does not take full advantage of our continuous scene representation. The main idea of Hierarchical samoling is that The density of the uniform sampled points shows where objects are more likely to exist in space. So we propose that every time after a uniform sampling, we perform a non-uniform sampling based on the density map.

## Slide 83
Fine sampling based on MCMC
Hierarchical Sampling
Notes: In this way, the points with higher density can be more fully sampled and trained. Here we shows how to numerically calculate the transient with ununiform sample points

## Slide 84: NeTF results
Notes: 2020 CVPR

## Slide 85: NeTF results
Notes: 2020 CVPR

## Slide 86
Results on Self-occluded Object
Notes: To further test the robustness of Neural transient field on occlusions, we experiment on a semi-occluded scene from ZNLOS dataset. Phasor Field is
most sensitive to occlusions. We could see that our method produces sharper edges of both front and back planes.

## Slide 87
Our Capture System
Notes: We also build our own capture system.

## Slide 88: NeTF results
Notes: 2020 CVPR

## Slide 89
Contributions
A novel neural modeling framework for NLOS imaging.
A forward model under spherical coordinate system.
Two-stage training and hierarchical sampling to improve performance.
MLP
Notes: To summarize, we present a novel neural modeling framework called Neural transient fields for NLOS imaging using a multi-layer perceptron. Due to the property of light propagation in NLOS, We formulate the systm under spherical coordinates. We also propose two training strategies to improve performance,.
We believe that Neural transient fields demonstrates that deep learning provides an alternative and potentially feasible solution to a broader class of inverse imaging problems.

## Slide 90: What else can NLOS do？
[9] Li, Zheng-Ping, et al. "Single-photon computational 3D imaging at 45 km." Photonics Research 8.9 (2020): 1532-1540.
Notes: 浦东民航大厦

## Slide 91: What else can NLOS do？
[9] Li, Zheng-Ping, et al. "Single-photon computational 3D imaging at 45 km." Photonics Research 8.9 (2020): 1532-1540.
Notes: K11购物艺术中心

## Slide 92: What else can NLOS do？
[10] Wu, Cheng, et al. "Non–line-of-sight imaging over 1.43 km." Proceedings of the National Academy of Sciences 118.10 (2021): e2024468118.
Notes: K11购物艺术中心

## Slide 93: What else can NLOS do？
[10] Wu, Cheng, et al. "Non–line-of-sight imaging over 1.43 km." Proceedings of the National Academy of Sciences 118.10 (2021): e2024468118.
Notes: K11购物艺术中心

## Slide 94: What else can NLOS do？
[11] Liu, et al. "HiddenPose: Non-Line-of-Sight 3D Human Pose
Estimation."
Notes: K11购物艺术中心

## Slide 95: What else can NLOS do？
[12] Metzler, Christopher A., David B. Lindell, and Gordon Wetzstein. "Keyhole imaging: non-line-of-sight imaging and tracking of moving objects along a single optical path." IEEE Transactions on Computational Imaging 7 (2020): 1-12.

## Slide 96: What else can NLOS do？
[13] Lindell, David B., and Gordon Wetzstein. "Three-dimensional imaging through scattering media based on confocal diffuse tomography." Nature communications 11.1 (2020): 1-8.
Notes: K11购物艺术中心

## Slide 97: What else can NLOS do？
[14] Cao, Ruizhi, et al. "High-resolution non-line-of-sight imaging employing active focusing." Nature Photonics (2022): 1-7.
Notes: K11购物艺术中心

## Slide 98: Future directions
Faster and more robust algorithm
System with higher resolution
More applications
Notes: 2020 CVPR