## Slide 1: NeRF & CT Imaging
Qing Wu
wuqing@shanghaitech.edu.cn
ShanghaiTech University

## Slide 2: Computed Tomography (CT)
CT Images
Human Body

## Slide 3: The Standard Pipeline of CT acquisition
Projecting X-rays from multiple views
Reconstructing CT image via filtered back-projection (FBP)
Sinogram
CT image
CT scanner

## Slide 4: Two Problems in CT acquisition
Radiation caused by X-rays
  2-3 times a year
Subjection motion and CT scanner’s error

## Slide 5: Sparse-View (SV) CT for Reducing Radiation
Reducing the number of projection views
180 views
30 views
6x

## Slide 6: SVCT for Reducing Radiation
The central slice theorem

## Slide 7: SVCT for Reducing Radiation
SV projections result in severe streaking artifacts
180 views
30 views

## Slide 8: Supervised Method for SVCT
Image-domain based models (Image Denoising)
Sinogram-domain based models
Cross-domain based models
FBP
SV Sinogram
Low-quality
CT image
CNN Model
Artifacts-free
CT image

## Slide 9: Supervised Method for SVCT
Image-domain based models
Sinogram-domain based models (Image Interpolation)
Cross-domain based models
FBP
SV Sinogram
CNN Model
Artifacts-free
CT image
DV Sinogram

## Slide 10: Supervised Method for SVCT
Image-domain based models
Sinogram-domain based models
Cross-domain based models (Image Translation)
SV Sinogram
CNN Model
Artifacts-free
CT image

## Slide 11: Supervised Method for SVCT
Two Common Limitations
  Need for a large-scale dataset
  Model generalization (Types of X-ray Beam)

## Slide 12: Supervised Method for SVCT
Two Common Limitations
  Need for a large-scale dataset
  Model generalization (CT scanners)
Siemens
GE
Philips
United Imaging

## Slide 13: Motivation
Recovering high-quality CT images from the acquired SV sinograms without extra data
Model
SV Sinogram
Artifacts-free
CT image

## Slide 14: Neural Radiance Field (NeRF)
Synthesizing arbitrary views

## Slide 15: Neural Radiance Field (NeRF)
Representing the field (3D object) as a continuous function
Based on the 2D images, using an MLP to learn the function.
3D coordinate
Color (RGB)
2D direction
Density

## Slide 16: Neural Radiance Field (NeRF)
Pipeline
field (3D object) domain
measurement (image) domain

## Slide 17: Neural Radiance Field (NeRF)
Main commons and differences between view synthesis and SVCT
Input: 2D images
Output: 2D images
Input: 2D projections
Output: 3D volume

## Slide 18: NeRF-based SVCT Models
CoIL (10.1109/TCI.2021.3125564)
NAF (10.1007/978-3-031-16446-0_42)
SCOPE (10.48550/arXiv.2209.05483)

## Slide 19: CoIL: Coordinate-Based Internal Learning
Represent the sinogram as a continuous function:
Projection view
Projection
value
X-ray Position
Sinogram

## Slide 20: CoIL: Coordinate-Based Internal Learning

## Slide 21: CoIL: Coordinate-Based Internal Learning

## Slide 22: NAF: Neural Attenuation Fields

## Slide 23: NAF: Neural Attenuation Fields

## Slide 24: NAF: Neural Attenuation Fields

## Slide 25: SCOPE: Self-Supervised Coordinate Projection Network
Following original NeRF will produce many noises in results

## Slide 26: SCOPE: Self-Supervised Coordinate Projection Network

## Slide 27: SCOPE: Self-Supervised Coordinate Projection Network

## Slide 28: SCOPE: Self-Supervised Coordinate Projection Network

## Slide 29: SCOPE: Self-Supervised Coordinate Projection Network

## Slide 30: SCOPE: Self-Supervised Coordinate Projection Network

## Slide 31: Summary for NeRF-based SVCT methods
Data Requirements
  Only require a single SV sinogram
Performance
  Produce robust performance for diverse CT settings.
  Outperforms supervised deep learning models
Speed
  Take 1 min for a CT image of 512*512 on a single NVIDIA RTX 3060 GPU

## Slide 32: SVCT with Rigid Motion
Subjection motion and CT scanner’s error

## Slide 33: SVCT with Rigid Motion
Optimizing pose and neural network simultaneously

## Slide 34: SVCT with Rigid Motion

## Slide 35: Thanks！
Qing Wu
wuqing@shanghaitech.edu.cn
ShanghaiTech University