## Slide 1
AI application in cryo-ET
沈盈君

## Slide 2
Cryo-EM workflow

## Slide 3
Cryo-ET workflow

## Slide 4
Motion correction

## Slide 5
Motion correction model

## Slide 6
Motioncor2--global correction
The global motion is corrected iteratively by calculating cross correlation of each sub-frame against the sum of all other sub-frames based upon the alignment of the previous iteration.

## Slide 7
Motioncor2--doming model
When the electron beams hit the sample, sample will have a significant motion pendicular to the sample plane.
This motion is considered sperately at different local regions. Thus, frames are divided into patches after global correction.

## Slide 8
Motioncor2--doming model
In theory, the local motion is different on each pixel. So the patch should be small as possible.
But due to the extremely low SNR, motion will be corrected with low accuracy if patch is too small.

## Slide 9
Motioncor2--doming model
Benefits:
eliminate checkboard artifact
more complete motion
smooth

## Slide 10
Motioncor2--doming model

## Slide 11
Motioncor2--doming model
The measured global shifts are corrected by phase shifting in the Fourier domain to yield a global-motion-corrected stack.
The local shifts are done in real space and use bilinear interpolation. The final image is obtained by cropping the corrected sum in Fourier domain to the user specified resolution.

## Slide 12
Motioncor2--dose weighting
Weighting movie frames with respect to the dose.

## Slide 13
Motioncor2--dose weighting
Down-weighting movie frames with high dose can generate better result.
But, it may attenuates the high resolution Thon ring signals use for CTF estimation.

## Slide 14
Motioncor2--dose weighting

## Slide 15
So MotionCor2 produce both results. Weighted one for the following reconstruction and unweighted for CTF estimation.

## Slide 16
Cryo-ET workflow

## Slide 17
Cryo-ET reconstruction
Cryo-ET’s difference from traditional NeRF:
parallel rays (not pinhole camera)
density-only projection (not volume rendering)

## Slide 18
Cryo-ET reconstruction--WBP
CTF Thon ring
original image
FFT

## Slide 19
Cryo-ET reconstruction--SIRT filter

## Slide 20
Cryo-ET reconstruction--WBP
CTF Thon ring
sirt image
FFT

## Slide 21
Cryo-ET reconstruction--WBP result
WBP reconstruction slice
FFT

## Slide 22
Recall: subtomo averaging

## Slide 23
Cryo-ET reconstruction--WBP subtomo result

## Slide 24
Cryo-ET reconstruction
Actually, there’re almost NO deep learning method about cryo-ET 3D reconstruction.
For EM, it is CryoDRGN, because there’re thousands of images with different poses to do fourier space reconstruction.
For ET, there’re only sparse-view images with limited angle, not suitable in fourier space.

## Slide 25
Cryo-ET workflow

## Slide 26
Denoise
Since both Cryo-ET and Cryo-EM have extremely low SNR, denoising is an important way to enhance data analysis quality with great potential.
But denoise is challenging in Cryo-EM/ET:
very high noise level
no ground truth clean image
hard to find a prior noise model

## Slide 27
Denoise--N2N

## Slide 28
Denoise--N2N theory
Assume that we have a set of unreliable measurements of the room temperature.
Then, to estimate the true temperature , the function below is optimized:
If loss function is L2 loss, then
If loss function is L1 loss, then median of observation.

## Slide 29
Denoise--N2N theory
For a neural network with input-target pair , the task is:
The full task can be decomposed to the same minimization problem at every training sample:

## Slide 30
Denoise--N2N theory
The key of N2N: Training a neural network from low dimension to high dimension using L2 loss, the network is expected to output the average of all possible result.
For optimization target above, if we corrupt input-conditioned target distributions with a zero-mean noise. The network is still supposed to learn that value.
where are now drawn from corrupted distribution, conditioned on clean target such that .

## Slide 31
Denoise--N2N pipeline
input
corrupt with zero-mean noise
corrupt with zero-mean noise
input
target
U-net
loss
prediction

## Slide 32
Denoise--N2N setup
Case 1: 100 pairs, each pair 20 images(1 clean + 19 noisy), clean target supervised
Case 2: 100 pairs, each pair 20 images(1 clean + 19 noisy), clean/noisy pairs N2N
Case 3: 1000 pairs, each pair 2 images(2 noisy), N2N

## Slide 33
Denoise--N2N result
For input-conditioned noise, the L2 loss achieves better result.

## Slide 34
Denoise--N2N result

## Slide 35
Denoise--N2N result
, with decrease from 2 to 0 during training

## Slide 36
Denoise--N2N analysis
For L2 loss, the expected difference between means from corrupted and clean target is:
N2N has limits:
Need a big amount of paired noisy data (impossible in many scenario)
Need the noise to be zero-mean
High noise level will harm the performance

## Slide 37
Denoise--N2V

## Slide 38
Denoise--N2V theory
blind-spot receptive field

## Slide 39
Denoise--N2V theory
In N2V, using blind-spot training means to optimize:
which enables single image denoising.
In N2N, if single noisy images are used instead of paired noisy images, the CNN network will finally only focus on the target pixel and ignore the pixels around.

## Slide 40
Denoise--N2V setting

## Slide 41
Denoise--N2V result

## Slide 42
Denoise--N2V result (failure case)
impulse point
structure noise

## Slide 43
Denoise--N2V vs N2N
N2N | N2V
paired noisy image | single noisy image
zero-mean noise | zero-mean noise
various types of noise model | only input-dependent noise
Fortunately, in cryo data, we have movie frames.

## Slide 44
Denoise--Topaz

## Slide 45
Denoise--Topaz pipeline
N2N-based pipeline

## Slide 46
Denoise--Topaz dataset

## Slide 47
Denoise--Topaz result

## Slide 48
Denoise--Topaz result
L1 is slightly better than L2 in small model
Full Unet with L2 loss and large dataset performs best.

## Slide 49
Denoise--Topaz result
raw
Topaz

## Slide 50
Denoise--Topaz result
Topaz denoise improves interpretability and picking of difficult particle projections

## Slide 51
Denoise--Topaz result
randomly select 1000 particles to reconstruct
Topaz denoised particles are less reliable.

## Slide 52
Denoise--Topaz result
Topaz denoise enhances SNR of short exposure micrographs.

## Slide 53
Denoise--Topaz pipeline (3D)
WBP odd reconstruction
3D U-net
split
even frames data
WBP even reconstruction
loss
3D U-net
odd frames data
denoised odd volume
denoised even volume

## Slide 54
Denoise--Topaz result (3D denoise)

## Slide 55
Denoise--Topaz limitation
Topaz denoise has several limitation:
requirement for large datasets
denoised images/volumes may have hallucinated signal which will harm the high frequency signal.
“we recommend that Topaz-Denoise models be used to assist with visualization and object identification, then the objects of interest be extracted and processed from raw micrographs/tomograms.”

## Slide 56
Denoise--other AI application on ET
based on N2V
based on N2N (noisier2noise)

## Slide 57
Cryo-ET workflow

## Slide 58
cryo-ET particle picking

## Slide 59
cryo-ET particle picking
In Cryo-EM, 2D particle picking is essential for classification and reconstruction, particle are 2D images.
In Cryo-ET, particle is picked after reconstruction, particles are 3D volumes.

## Slide 60
cryo-ET particle picking

## Slide 61
cryo-ET particle picking
Both strategies have label noise problem

## Slide 62
cryo-ET particle picking result

## Slide 63
cryo-ET particle picking result

## Slide 64
cryo-ET particle picking result